## Slide 1: DSD Final Presentation (MIPS)
B05901013 張景皓
B05901014 吳靖平

## Slide 2: Table of Contents
Baseline
  J/JR/JAL/JALR
  BEQ/BNE
  Forwarding
  Stall
  Cache
Extensions
  BrPred
  L2 Cache
  MultDiv
Collaboration

## Slide 3: Baseline

## Slide 4: Overall Architecture

## Slide 5: Jump-related Instructions

## Slide 6: Implemented Instructions
MIPS Instruction | Op/funct | Operation
j destination | 2 | PC = address * 4
jal destination | 3 | $ra = PC; PC = address * 4
jr $rs | 0/8 | PC = $rs
jalr $rt $rs | 0/9 | $rt = PC; PC = $rs

## Slide 7: Flush IF/ID
//IF_ID is stalled to refetch new instruction when nop_FD is HIGH
assign nop_FD = (Jump[1] ^ Jump[0]) ? 1'b1 : 1'b0;
// j/jal: Jump = 2’b01
//jr/jalr: Jump = 2’b10
Notes: Jump-related instructions的解碼發生在ID stage，也表示同時間IF stage所讀取的指令為PC+4而非jump所指到的PC。所以凡是讀到j/jr/jal/jalr等指令，IF/ID的gate所存取的值必須要flush，重新讀取新指令(jump destination)，如此才不會執行到錯誤的指令

## Slide 8: Forwarding

## Slide 9: Forwarding Conditions
assign ForwardAD = (RegWrite_IE & (RegisterRd_IE != 5'b0) & (RegisterRd_IE == RegisterRs_FD)) ? 2'b11 : (RegWrite_EM & (RegisterRd_EM != 5'b0) & (RegisterRd_EM == RegisterRs_FD)) ? 2'b10 : (RegWrite_MW & (RegisterRd_MW != 5'b0) & (RegisterRd_MW == RegisterRs_FD)) ? 2'b01 : 2'b00;
assign ForwardBD = (RegWrite_IE & (RegisterRd_IE != 5'b0) & (RegisterRd_IE == RegisterRt_FD)) ? 2'b10 : (RegWrite_MW & (RegisterRd_MW != 5'b0) & (RegisterRd_MW == RegisterRt_FD)) ? 2'b01 : 2'b00;
assign ForwardAE = (RegWrite_EM & (RegisterRd_EM != 5'b0) & (RegisterRd_EM == RegisterRs_IE)) ? 2'b10 : (RegWrite_MW & (RegisterRd_MW != 5'b0) & (RegisterRd_MW == RegisterRs_IE)) ? 2'b01 : 2'b00;
assign ForwardBE = (RegWrite_EM & (RegisterRd_EM != 5'b0) & (RegisterRd_EM == RegisterRt_IE)) ? 2'b10 : (RegWrite_MW & (RegisterRd_MW != 5'b0) & (RegisterRd_MW == RegisterRt_IE)) ? 2'b01 : 2'b00;
Notes: 我們最初的寫法是參照講義的內容，但是後來發現判斷條件會不夠完整，應該在EX/MEM/WB每個階段之間都要加上forwarding datapath。以ForwardAD來說，ID/EX、EX/MEM、MEM/WB都有forwarding的判斷條件使data可以從各個stage直接送回ID stage。

## Slide 10
Adjusted Forwarding Unit
00
01
11
10
00
01
11
10

## Slide 11: Cache

## Slide 12: Specification
Instruction Cache
  Mode: read-only (ICACHE_ren = 1’b1; ICACHE_wen = 1’b0)
  Size: 32 words (8 blocks * 4 words)
  Approach: direct mapping
  Write policy: write back
Data cache
  Mode: read/write available
  Size: 32 words (8 blocks * 4 words)
  Approach: direct mapping
  Write policy: write back

## Slide 13: FSM

## Slide 14: Why not 2-way associative cache?
 | area (um^2) | testbench clock (ns) | operation time (ns) | cycle | sdc (ns)
Direct mapping | 249159 | 4.47 | 8187.19 | ~1832 | 3
2-way associative | 258395 | 6.01 | 10905 | ~1818 | 3.5
Notes: 我們是直接使用HW4寫過的cache。Direct mapping與2-way associative兩個版本都有合成，但2-way合成出來結果不甚理想，連cycle = 6(ns)都過不了，因此最終決定使用direct mapping的版本作為Baseline MIPS的cache。

## Slide 15: Extensions

## Slide 16: Branch Prediction

## Slide 17: Architecture

## Slide 18: 1-bit predict

## Slide 19: 2-bit predict

## Slide 20: RTL simulation results comparison
Model | a=10, b=20, c=30 | a=1, b=50, c=1 | a=1, b=1, c=50
Baseline | 320 | 377 | 230
1-bit predict | 305/306 | 419/418 | 178/177
2-bit predict | 313/313/314/315 | 426/372/371/371 | 184/178/176/176
a = # of always not taken
b = # of interleaved branch
c = # of always taken
# of cycles

## Slide 21: Gate-level simulation results comparison
a = 10, b = 20, c = 30
Model | sdc cycle(ns) | area(um^2) | tb pass cycle(ns) | total execution time(ns)
Baseline | 3 | 249159 | 4.57 | 1541
1-bit predict | 3.1 | 259936 | 4.2 | 1341
2-bit predict | 3 | 267800 | 3.51 | 1149

## Slide 22: Gate-level simulation results comparison
has Hazard
Model | sdc cycle(ns) | area(um^2) | tb pass cycle(ns) | total execution time(ns)
Baseline | 3 | 249159 | 4.43 | 8187
1-bit predict | 3.1 | 259936 | 4.91 | 9443
2-bit predict | 3 | 267800 | 5.05 | 9596

## Slide 23: L2 Cache

## Slide 24: A unified 2-way associative cache
Total 256 words, 4 words for 1 block, 64 blocks in total
Approach: 2-way associative
Write policy: write back
Replacement policy: LRU (Least Recently Used)

## Slide 25: Details in replacement
L2 cache is an unified cache, which means simultaneous access to same block could happen. In this situation, conditions for updating LRU should be specified. In our design, we always make the block storing D memory data the LRU block. This is because that since the instruction is usually fetched in order, normally it will be accessed on the next cycle, hence we should prevent it from being flushed.
if(proc_addr_D[BLOCK_WIDTH-1:0]==proc_addr_I[BLOCK_WIDTH-1:0])begin
block_LRU[proc_addr_D[BLOCK_WIDTH-1:0]] <= (proc_addr_D[27:BLOCK_WIDTH]==block_tag[proc_addr_D[BLOCK_WIDTH-1:0]][TAG_WIDTH-1:0])?1'b0:1'b1;//treat D read hit as LRU
end

## Slide 26: FSM

## Slide 27: miss rate
n=20 / n=30
cache | # of access | # of miss | miss rate(%)
I cache | 30545/67435 | 20/20 | 0.07/0.03
D cache | 6587/14707 | 3144/9734 | 47.73/66.19
L2 cache | 1310/3405 | 37/47 | 2.82/1.38
n = 20: 40934 → 35914 (# of cycles)
n = 30: 93333 → 79993 (# of cycles)

## Slide 28: gate-level simulation results comparison
n=20 / n=30
Model | sdc cycle(ns) | area(um^2) | tb pass cycle(ns) | total execution time(ns)
L2 cache | 10 | 849752 | N/A | N/A
L2 cache | 5 | 778617 | N/A | N/A
L2 cache | 4 | 809814 | 5.71 | 205636/457825
L2 cache | 3.5 | 856394 | 5.75 | 207074/461027
L2 cache | 3.3 | 856394 | 5.75 | 207074/461027
Baseline | 3 | 249159 | 4.57 | 199470/458648

## Slide 29: Multiplication/Division

## Slide 30: Implemented Instructions
MIPS Instruction | Op/funct | Operation
mult $rs $rt (signed) | 0/24 | {$HI, $LO} = $rs*$rt
div $rs $rt (signed) | 0/26 | {$HI, $LO} = {$rs%$rt, $rs/$rt}
mfhi $rd | 0/16 | $rd = $HI
mflo $rd | 0/18 | $rd = $LO

## Slide 31: Multiplier/Divider Architecture (I) Verilog Arithmetic Operators
MULT: begin
result_o = 32'b0;
{HI_o, LO_o} = $signed(data1_i) * $signed(data2_i);
end
DIV: begin
result_o = 32'b0;
HI_o = $signed(data1_i) % $signed(data2_i);
LO_o = $signed(data1_i) / $signed(data2_i);
end

## Slide 32: Multiplier/Divider Architecture (II) Iterative Multiplication
if (product[0]) begin //1
if (count != 6'd31) next_product = $signed({product[63:32] + multiplicand, product[31:0]}) >>> 1'b1;
else next_product = $signed({product[63:32] + ~multiplicand + 1'b1, product[31:0]}) >>> 1'b1; //last shift-and-add
end else next_product = $signed(product) >>> 1'b1; //0

## Slide 33: Multiplier/Divider Architecture (II) Iterative Division
if (count < 6'd32) begin
{next_remainder, next_quotient} = diff_positive ? {difference, quotient[30:0], 1'b1} : {shifted_remainder, quotient[30:0], 1'b0};
end else begin //negate the sign of quotient and remainder if negative
next_quotient = quotient_sign ? ~quotient + 1'b1 : quotient;
next_remainder = remainder_sign ? ~remainder + 1'b1 : remainder;
end
Convert dividend and divisor to positive
Perform unsigned division
Quotient sign = dividend sign XOR divisor sign
Remainder sign = dividend sign
Negate the sign of quotient and remainder if their signs are negative

## Slide 34: Multiplier Architecture (III) Radix-4 Booth Encoding
X_2i+1 | X_2i | X_2i-1 | Operation
0 | 0 | 0 | +0
0 | 0 | 1 | +y
0 | 1 | 0 | +y
0 | 1 | 1 | +2y (<<1)
1 | 0 | 0 | -2y (<<1)
1 | 0 | 1 | -y
1 | 1 | 0 | -y
1 | 1 | 1 | -0
Only 4 cycles needed for 8-bit multiplication

## Slide 35: Multiplier Architecture (III) Radix-4 Booth Encoding Example
(-3) * (-7) = 1101 * 1001 (y * x) = 00010101 = 21 -> 2 cycles operation
{1001, 0} -> 100 (-2y), 010(+y)
1101
x) -2+1
---------
11111101
00011000
-----------
00010101

## Slide 36: Non-algorithmic optimization
Multiplication
  multiplicand/multiplier == 0
  multiplicand/multiplier == 1
  multiplicand/multiplier == 2, 4, 8, … (2^n) -> shift left logic
Division
  dividend == 0
  dividend == divisor
  divisor == 1
  divisor == 2, 4, 8, … (2^n) -> shift right logic

## Slide 37: Overall Comparison
 | area (um^2) | testbench clock (ns) | operation time (ns) | cycle | sdc (ns)
Arithmetic Operator (*, /, %) | ~590000 | N/A | N/A | N/A | 10
Iterative Approach | 268584.69 | 4.71 | 3707.55 | ~787 | 3.5
Optimized Iterative Approach | 278926.95 | 4.17 | 2100.44 | ~504 | 3.2
Booth encoding multiplier + Iterative divider | 284726.97 | 4.21 | 1917.98 | ~456 | 3

## Slide 38: 42% cycle reduction
achieved by Booth-encoding (787 -> 456)
Operation time < 2 (us)
6% area increase (268000 -> 284000)

## Slide 39: Collaboration

## Slide 40
B05901014 吳靖平 | B05901013 張景皓
Baseline: cache | Baseline: other modules
Baseline: connect modules (i_MIPS) | Baseline: logic synthesis
Baseline: troubleshooting | Baseline: troubleshooting
Extension: BrPred | Extension: MultDiv
Extension: L2 Cache |