## Slide 1: Extension: Two-Level Cache
Specifications

## Slide 2: Extension Description (1/2)
Main Goal
  Add 2 separate L2 caches for I-cache and D-cache
  Unified L2 cache (1 L2 cache for both L1 I-cache & L1 D-cache) will be considered as better design (but not required)
Total size of respective L1 cache is suggested to be 32 words
  8 blocks & each 4 words
Total size of L2 caches (I + D) are suggested to be 256 words
  Block size and number of blocks are up to your considerations

## Slide 3: Extension Description (2/2)
System Clock Speed
  L1 Caches, L2 Caches, Slow Memory : Same clock speed as MIPS
I/O Specification
  Refer to the same top module as baseline: add ‘module L2_Cache’
  “Unified L2 cache” is better than “Separate L2 caches”

## Slide 4: Test Program Generation
Based on “hasHazard”, but long version
  Generate Fibonacci sequence with increment (F1, F1+1, … F1+N, F2, F2+1, …)
In file “generate”:
  L2Cache_generate.py
    Python (version = 3.x)
    Modify the parameters in the code
    I_mem_L2Cache_ref & TestBed_L2Cache_ref should be placed in the same folder
    I_mem_L2Cache & TestBed_L2Cache will be generated
      Provieded files nb20incre3
+define+L2Cache in ncverilog simulation command

## Slide 5: Comparison Metrics
Base on the test program: “I_mem_L2Cache”
Score 1 (L2C_S1): Avg. memory access time (ns)
  L2C_S1 = HT1 + MR1*(HT2+MR2*MP2)
  HT: hit time
  MR: miss rate
  MP: miss penalty
  ~1: of level 1 cache
  ~2: of level 2 cache
Score 2 (L2C_S2): Total execution time (ns)
  L2C_S2 = total execution time of the test program
Don’t worry about the performance evaluation. It is just one of the criteria. Focus more on what you design to solve problems you face.

## Slide 6: Some Possible Discussion
Design methodology for good score (before/after)
The size ratio of L2 Cache to L1 Cache
Sequence length for demonstrating the effectiveness of L2 Cache